## Slide 1: WinFACT
Soft - PLC

## Slide 2: Features
Development environment
IL (instruction list)
Intelligent automatic code completion
Fast compiler
Debugging options like breakpoints, evaluation of
variables and detecting of memory changes
Saving of views
Instructions according to IEC 61131- 3
Implicitly type casting
Standard function blocks
Exception and error handling options
Syntax highlighting

## Slide 3: Development environment
Editor with syntax highlighting
Automatic code completion
Buttons for the debugging mode...
…and the quick displaying and hiding of further windows like…
Saving the view of the development environment as well as...
…deleting and...
…adjusting the view.
Message window for compiler messages

## Slide 4: IL
0..49d_17h_2m_47s_295ms; resolution 1 ms
32Bit
TIME
-1.2E-38 .. 1.2E38; precision (decimal): 6 digits
32Bit
REAL
-2147483648..2147483647
32Bit
DINT
-32768..+32767
16Bit
INT
0..4294967296
32Bit
DWORD
0..65535
16Bit
WORD
0..255
8Bit
BYTE
true, false
1Bit
BOOL
Range
Size
Type
Data types

## Slide 5: Available instructions
Loading / Saving
Bitwise operations
Shift operations
Comparisons
Arithmetic functions
Numeric functions
Jumps
Callings of function blocks
Type casting instruction
LD, LDN,
ST, STN,
STC, STCN
AND, OR, XOR,
ANDN, ORN,XORN,
AND(, OR(, XOR(,
ANDN(, ORN(, XORN(,
NOT
SHL, SHR
ROL, ROR
LT, LE, EQ, NE, GE, GT
LT(, LE(, EQ(, NE(, GE(, GT(
ADD, SUB, MUL, DIV, MOD
ADD(, SUB(, MUL(, DIV(, MOD(
ABS, NEG,
LN, LOG, EXP,
SQRT,
SIN, COS, TAN,
ASIN, ACOS, ATAN
JMP, JMPC, JMPCN,
JMPL,
RET, RETC, RETCN
CAL, CALC, CALCN
xxxx_TO_yyyy
for all xxxx unequal yyyy
not existent: BOOL_TO_TIME

## Slide 6: Stand–Alone-PLC
Operates always as DDE-Server:
Inputs: r / w
Outputs: r / -
Support of all WinFACT drivers
OLE for Process Control
Data exchange with the Flexible Animation Builder for visualization purposes

## Slide 7: Soft-PLC under BORIS
During the debugging process
- breakpoint
- current row of execution
There is no limitation to the number of PLC blocks
DDE, OPC, FAB and hardware drivers
by corresponding blocks

## Slide 8: Control and display elements (selection)

## Slide 9: Summary
Stand-Alone
Solution of primarily
open loop control problems
Only one PLC
instance possible
Signal conditioning
within the PLC
BORIS block
Solution of open loop and
closed loop control problems
Several PLC blocks
Signal conditioning
within the PLC or
by BORIS blocks
Common features
DDE
OPC
FAB
Hardware I/O-support
by specific hardware
drivers
Soft-PLC